## Slide 1: Optimize your Sample Preparation Workflow for PFAS Analysis

## Slide 2: Optimize your Sample Preparation Workflow for PFAS Analysis
Automate the Sample Prep Workflow
  Automate the Solid Phase Extraction Step
  Automate the Concentration/Evaporation Step
Automated, Semi-Automated SPE Extractions and Concentration
  Reduces Human Error
  Reduces Outside contamination
  Increase Throughput
  Reduces Labor
No Teflon
Use Hyphenated techniques to deliver consistent, reproducible results
Different configurations to handle Matrix type and Budget
Use any size cartridge

## Slide 3: Automated Solid Phase Extraction front end for LC/MS
EconoTrace® PFC
TurboTrace® PFC
LC/MS
Modular and Expandable
Designed for Different Matrices and Number of Samples to be run per week
Drinking Water Methods

## Slide 4: Semi-Automated Solid Phase Extraction PFAS/PFOS front end for LC/MS
EZPFC / SuperVap PFC 24
LC/MS
Low Cost, High Throughput Sample Prep

## Slide 5: System Components
No Teflon
Tubing - High Density Polyethylene
Fittings – Delrin
Cartridge Adapters – Medical Grade Polypropylene

## Slide 6: Can this Handle Dirty Samples?
Typical Cartridge can have problems!
6ml cartridge
  Doesn’t do well
  Frit Surface Area is to small
Yes, A Cartridge will work
25ml cartridge
  Does well
  3X the Frit Surface Area

## Slide 7: FMS, Inc. Plastic Filtration Wool
Glass/Plastic Wool
Irregular random stranding
Slows Particles to the Uniform Frit
Prevents Clogging

## Slide 8: Prepping the 6ml Cartridge with Plastic Filtration Wool
6ml Cartridge with Plastic Wool
Take a little and push it into the barrel of the syringe until it touches the cartridge Frit
The Sample will not clog, it will take longer to process

## Slide 9: Live Instruments

## Slide 10: Sample Bottle Filter

## Slide 11: Dirty Sample from a Customer

## Slide 12: Industrial 433 Matrix 250ml

## Slide 13: 6ml and 25ml Cartridges

## Slide 14: 250 ml run to completion on 6 ml cartridge with Plastic Wool

## Slide 15: 250ml run to completion 25ml cartridge

## Slide 16: TurboTrace PFC Automated Extraction and Concentration for PFAS/PFOS in Drinking Water and WasteWater
LC/MS
TurboTrace® PFC
Wastewater, Particulate Laden Samples
Drinking water Samples
Vacuum Pump or Positive Pressure for loading samples
Positive Pressure Pumping for conditioning, rinsing and elution
Direct to SuperVap Concentrator

## Slide 17: TurboTrace for Extraction and Concentration of PFAS/PFOS in Drinking/WasteWater
Modular and Scalable expandable from 1 to 4 Modules
Run 2 to 8 samples
Each Module can Run 2 Samples in parallel
Uses Positive Pressure Pumping
for Precise delivery of Elution and Wash Solvent
One valve pathway to the cartridge
Uses a Vacuum with liquid sensor to Load Dirty Samples and detect when finished
Direct Extract delivery to Concentrator for Evaporation
Fully Automated from start to finish

## Slide 18
Organic
Waste
Pump
Pressure Tr.
Aqueous
Waste
Vacuum
pump
Sample
Automated 1633 EPA method:
30psi
5psi
Rinse
Drinking Water
30psi
Solvents 1-6
FRC
OW
AQW
BYPS
RNS
CRT
N2
ORG
Regulators
SAM
5psi
Fraction
Wastewater
New SPE-Turbo

## Slide 19: Automated Extraction and Concentration for PFAS/PFOS in Drinking Water
EconoTrace® PFC
LC/MS
Drinking Water, Serum, and samples with minimal particulate
Positive Pressure Pumping

## Slide 20: EconoTrace SPE
Six Elution and Wash Solvents
Automatic Bottle Rinse
Sample Size 2 ml to unlimited
Touch Screen Control
SD Card for Storing and Transferring Methods
Nitrogen Drying
Direct to 15 ml Centrifuge tube Concentration

## Slide 21: EconoTrace for Extraction and Concentration of PFAS/PFOS in Drinking Water
Modular and expandable from 1 to 4 Modules, 2 to 8 samples
High Throughput Runs
8 Sample Extractions in Parallel
Uses Positive Pressure Pumping only
for Precise delivery of
Conditioning Solvent,
Sample, Bottle Rinse and Elution Solvent
Automatic Bottle Rinse
Delivers extract directly to SuperVap Concentrator for final blowdown
Fully Automated

## Slide 22: Automated Concentration for PFAs
SuperVap PFC
  24 positions
  15ml Conical vials
  No Teflon

## Slide 23: EPA 537.1
Chart: Percentage Recovery
| PFBS | PFHxA | GenX | PFHpA | PFHxS | ADONA | PFOA | PFNA | PFOS | 9Cl-PF3ONS | PFDA | N-MeFOSAA | PFUdA | N-EtFOSAA | 11Cl-PF3OUDS | PFDoA | PFTrDA | PFTeDA (PFTA)
2 ppt | 94 | 99 | 102 | 99 | 95 | 90 | 116 | 95 | 93 | 88 | 91 | 93 | 93 | 95 | 86 | 90 | 86 | 84
50 ppt | 99 | 109 | 123 | 103 | 102 | 104 | 103 | 110 | 101 | 100 | 111 | 92 | 108 | 98 | 91 | 101 | 93 | 93

## Slide 24: EPA 533
Chart: Percentage Recovery
| 11Cl-PF3OUdS | 9Cl-PF3ONS | ADONA | HFPO-DA (GenX) | NFDHA | PFBA | PFBS | 8:2FTS | PFDA | PFDoA | PFEESA | PFHpS | PFHpA | 4:2FTS | PFHxS | PFHxA | PFMPA | PFMBA | PFNA | 6:2FTS | PFOS | PFOA | PFPeA | PFPeS | PFUnA
 | 104 | 86.9401 | 80.1964 | 78.6821 | 97 | 101.2 | 86.437 | 96 | 89.5123 | 80.6403 | 98 | 100.2 | 83 | 98 | 91.9534 | 101.2 | 98 | 101 | 81.3283 | 99 | 86.2464 | 85.7099 | 104.3 | 92.8 | 101.6

## Slide 25: PFAS Background
Compound | Amount Spiked ng/L |  | Mean Percent Recovery | Background from FMS SPE
Perfluorinated Compounds | 50 ng/L |  |  | 50 ng/L
PFHxA |  | 61% |  | 0.068
PFHxS |  | 77% |  | 0.06
PFOA |  | 88% |  | 0.214
PFNA |  | 74% |  | 0.062
PFOS |  | 72% |  | 0.048
PFDA |  | 84% |  | 0.054
PFUdA |  | 65% |  | 
PFDoA |  | 57% |  | 0.011
Chart: PFAS native background
| PFBA | PFBS | PFPeA | PFHxA | PFHxS | PFHpA | PFOA | PFOS | PFNA | PFDA | PFDS | PFUnA | PFDoA | PFTrA


 | 0.04 | 0.01 | 0.03 | 0.02 | 0.01 | 0.05 | 0.04 | 0.03 | 0.02 | 0.01 | 0.04 | 0.03 | 0.01 | 0.01


## Slide 26: TurboTrace Parallel Sequential PFC Automated Extraction and Concentration for PFAS/PFOS in Drinking Water and WasteWater
LC/MS
TurboTrace® PFC Parallel Sequential
Wastewater, Particulate Laden Samples
Drinking Water Samples
Vacuum Pump or Positive Pressure for loading samples
Positive Pressure Pumping for conditioning, rinsing, and elution
Direct to SuperVap Concentrator

## Slide 27: TurboTrace for Extraction and Concentration of PFAS/PFOS in WasteWater
Modular and Scalable expandable from 1 to 6 Modules
Run 1 to 6 samples simultaneously, up to 30 sequentially
Each Module can Run 5 Samples in a Sequence
Uses Positive Pressure Pumping
for Precise delivery of
Elution and Wash Solvent
Uses Vacuum with liquid sensor to Load Dirty Samples
Direct Extract delivery to Concentrator for Evaporation
Fully Automated

## Slide 28
1633 Parallel-Sequential Recoveries (n=5)
Chart: Percent recovery
| PFBA | PFPeA | PFHxA | PFHpA | PFOA | PFNA | PFDA | PFUnA | PFDoA | PFTrDA | PFTeDA | PFBS | PFPeS | PFHxS | PFHpS | PFOS | PFNS | PFDS | PFDoS | 4:2FTS | 6:2FTS | 8:2FTS | PFOSA | NMeFOSA | NEtFOSA | NMeFOSAA | NEtFOSAA | NMeFOSE | NEtFOSE | HFPO-DA | ADONA | PFMPA | PFMBA | NFDHA | 9Cl-PF3ONS | 11Cl-PF3OUdS | PFEESA | 3:3 FTCA | 5:3 FTCA | 7:3 FTCA
 | 94 | 93 | 97 | 96 | 99 | 93 | 112 | 98 | 96.6519 | 100 | 86 | 67 | 91 | 101 | 87 | 102 | 96 | 88 | 75 | 96 | 83 | 92 | 101 | 91 | 90 | 99 | 103 | 94 | 90 | 78 | 82 | 94 | 96 | 96 | 77 | 90 | 94.5009 | 101.3172 | 96.6965 | 95.4407

## Slide 29: Concentration Functionality
Designed for PFAS/PFOS Concentration
Accepts Extracts Directly from FMS Automated SPE systems
Self Installable
  Video unpacking, installation and training video
Preprogrammed with most common temperature settings
Direct to 15ml Centrifuge Tubes
Dry bath heating element
Time based endpoint

## Slide 30: Semi-Automated Solid Phase Extraction front end for LC/MS
EZPFC
LC/MS

## Slide 31: EZPFC®
EZPFC 12 sample
Drinking Water,
Wastewater,
Particulate laden samples

## Slide 32: EZPFC Semi Automated SPE
Low Cost
  Run and Concentrate a batch of 24 samples 2 to 3 hours
Self Installable
  Unpacking and Installation/training video
Easy to Operate
  No Computers or Electronics to fail or maintain
Semi - Automated
  Hyphenates the entire Solid Phase Extraction Process – Extraction, Bottle Rinse, Inline Drying and Direct to 15ml Centrifuge tube for easy Concentration
Fast
  The fastest sample processing available for SPE
  Run up to 12 samples simultaneously
  Vacuum for fast loading of large volume samples
  Unattended Sample loading walkaway time
Closed system
  Eliminate potential outside contamination

## Slide 33: EZPFC Semi Automated SPE
Efficient
  Uses all SPE cartridge sizes
  Dedicated manifold for cartridge conditioning and sample loading
  Dedicated manifold for extraction and extracts
  Separates Organic from Aqueous waste
  Vacuum cartridge drying, Nitrogen cartridge drying or combined
  Automated Bottle Rinse and Elution
  Inline Extract Drying
  Small number of components to clean

## Slide 34
Surrogate Recovery with EZPFC |  |  |  | 
1633 order | 230131 RT Order | Surrogate | EZPFC Avg Recovery | EZPFC %RSD
1 | 1 | 13C4-PFBA | 111 | 6%
2 | 2 | 13C5-PFPeA | 116 | 6%
3 | 4 | 13C5-PFHxA | 110 | 6%
4 | 7 | 13C4-PFHpA | 110 | 7%
5 | 9 | 13C8-PFOA | 107 | 6%
6 | 11 | 13C9-PFNA | 109 | 8%
7 | 13 | 13C6-PFDA | 106 | 9%
8 | 17 | 13C7-PFUnA | 104 | 10%
9 | 18 | 13C2-PFDoA | 93 | 10%
10 | 19 | 13C2-PFTeDA | 83 | 12%
11 | 5 | 13C3-PFBS | 106 | 6%
12 | 10 | 13C3-PFHxS | 105 | 11%
13 | 16 | 13C8-PFOS | 110 | 8%
14 | 3 | 13C2-4:2FTS | 99 | 15%
15 | 8 | 13C2-6:2FTS | 97 | 16%
16 | 12 | 13C2-8:2FTS | 105 | 19%
17 | 20 | 13C8-PFOSA | 142 | 15%
18 | 22 | D3-NMeFOSA | 114 | 12%
19 | 24 | D5-NEtFOSA | 70 | 16%
20 | 14 | D3-NMeFOSAA | 103 | 9%
21 | 15 | D5-NEtFOSAA | 111 | 14%
22 | 21 | D7-NMeFOSE | 87 | 6%
23 | 23 | D9-NEtFOSE | 76 | 10%
24 | 6 | 13C3-HFPO-DA | 111 | 7%
1633 EZPFC labeled surrogate recoveries

## Slide 35: 1633 natives IDC spikes concentrations and recoveries
 |  | In ng/L |  |  |  |  | Native spike recovered (%) |  |  |  |  |  |  | 
Name | Target Amount ng/L | IDC-1 | IDC-2 | IDC-3 | IDC-4 |  | IDC-1 | IDC-2 | IDC-3 | IDC-4 |  | Average | STDEV | RSD(%)
11Cl-PF3OUdS | 8.7 | 8.69 | 8.39 | 8.78 | 9.04 |  | 100 | 97 | 101 | 104 |  | 100 | 3.1 | 3.1
3-3 FTCA | 9.7 | 8.21 | 9.66 | 9.45 | 9.26 |  | 84 | 99 | 97 | 95 |  | 94 | 6.6 | 7.0
4-2 FTS | 9.6 | 9.53 | 9.39 | 8.96 | 8.84 |  | 99 | 98 | 93 | 92 |  | 96 | 3.4 | 3.6
5-3 FTCA | 52.0 | 48.65 | 52.44 | 52.01 | 52.74 |  | 94 | 101 | 100 | 101 |  | 99 | 3.7 | 3.7
6-2 FTS | 9.7 | 9.20 | 9.53 | 9.38 | 9.48 |  | 95 | 98 | 97 | 98 |  | 97 | 1.5 | 1.5
7-3 FTCA | 49.6 | 45.57 | 48.85 | 50.91 | 50.80 |  | 92 | 98 | 103 | 102 |  | 99 | 5.0 | 5.1
8-2 FTS | 10.0 | 8.65 | 9.39 | 10.08 | 9.85 |  | 86 | 93 | 100 | 98 |  | 94 | 6.3 | 6.7
9Cl-PF3ONS | 9.4 | 9.60 | 9.00 | 9.35 | 9.30 |  | 103 | 96 | 100 | 99 |  | 100 | 2.6 | 2.6
ADONA | 8.0 | 8.25 | 7.73 | 8.26 | 8.03 |  | 103 | 96 | 103 | 100 |  | 100 | 3.1 | 3.1
EtFOSE | 23.9 | 22.60 | 22.30 | 25.24 | 24.09 |  | 95 | 93 | 106 | 101 |  | 99 | 5.7 | 5.8
HFPO-DA | 9.3 | 9.31 | 9.34 | 9.24 | 9.34 |  | 100 | 100 | 99 | 100 |  | 100 | 0.5 | 0.5
MeFOSE | 21.6 | 21.94 | 22.76 | 23.26 | 22.26 |  | 102 | 106 | 108 | 103 |  | 105 | 2.7 | 2.6
N-EtFOSA | 2.0 | 2.25 | 1.84 | 2.04 | 2.19 |  | 113 | 92 | 102 | 110 |  | 104 | 9.2 | 8.8
N-EtFOSAA | 2.3 | 2.04 | 1.99 | 2.19 | 2.33 |  | 91 | 89 | 97 | 103 |  | 95 | 6.6 | 7.0
NFDHA | 5.2 | 4.51 | 4.76 | 4.97 | 4.86 |  | 87 | 92 | 96 | 94 |  | 92 | 3.8 | 4.1
N-MeFOSA | 2.4 | 2.26 | 1.95 | 2.33 | 2.27 |  | 95 | 82 | 98 | 96 |  | 93 | 7.2 | 7.8
N-MeFOSAA | 2.3 | 2.09 | 2.21 | 2.23 | 2.45 |  | 93 | 98 | 99 | 109 |  | 100 | 6.7 | 6.7
PFBA | 8.6 | 8.07 | 10.17 | 9.14 | 9.09 |  | 94 | 118 | 106 | 106 |  | 106 | 10.0 | 9.4
PFBS | 2.2 | 2.08 | 2.06 | 2.18 | 2.21 |  | 93 | 91 | 97 | 98 |  | 95 | 3.4 | 3.6
PFDA | 1.9 | 2.13 | 2.01 | 2.05 | 2.17 |  | 109 | 103 | 105 | 111 |  | 107 | 3.7 | 3.5
PFDoA | 2.3 | 2.11 | 2.30 | 2.20 | 2.45 |  | 92 | 100 | 96 | 106 |  | 98 | 6.2 | 6.3
PFDoS | 2.0 | 1.32 | 1.55 | 1.50 | 1.52 |  | 68 | 79 | 77 | 77 |  | 75 | 5.1 | 6.8
PFDS | 1.9 | 2.15 | 1.90 | 1.81 | 2.14 |  | 112 | 99 | 94 | 111 |  | 104 | 8.8 | 8.5
PFEESA | 5.2 | 4.91 | 5.12 | 5.39 | 5.41 |  | 94 | 97 | 103 | 103 |  | 99 | 4.6 | 4.6
PFHpA | 2.1 | 1.91 | 2.26 | 2.00 | 2.19 |  | 91 | 107 | 95 | 104 |  | 99 | 7.8 | 7.8
PFHpS | 2.0 | 2.24 | 2.19 | 2.08 | 2.24 |  | 110 | 108 | 102 | 110 |  | 108 | 3.7 | 3.5
PFHxA | 2.2 | 2.01 | 2.12 | 2.22 | 2.17 |  | 94 | 99 | 103 | 101 |  | 99 | 4.1 | 4.2
PFHxS | 2.2 | 1.94 | 1.93 | 2.11 | 2.13 |  | 90 | 89 | 98 | 99 |  | 94 | 5.0 | 5.3
PFMBA | 4.5 | 4.51 | 4.55 | 4.60 | 5.21 |  | 100 | 100 | 101 | 115 |  | 104 | 7.2 | 6.9
PFMPA | 4.2 | 3.56 | 4.01 | 4.10 | 3.62 |  | 85 | 96 | 98 | 87 |  | 92 | 6.6 | 7.2
PFNA | 2.2 | 1.78 | 2.07 | 2.03 | 2.41 |  | 80 | 93 | 91 | 108 |  | 93 | 11.6 | 12.4
PFNS | 2.0 | 1.93 | 2.00 | 1.83 | 2.24 |  | 98 | 101 | 93 | 114 |  | 101 | 8.8 | 8.7
PFOA | 2.3 | 1.99 | 2.21 | 2.25 | 2.31 |  | 85 | 95 | 96 | 99 |  | 94 | 6.0 | 6.4
PFOS | 1.8 | 2.10 | 1.94 | 2.09 | 2.16 |  | 116 | 108 | 116 | 120 |  | 115 | 5.1 | 4.4
PFOSA | 2.2 | 2.09 | 2.22 | 2.11 | 2.17 |  | 97 | 103 | 98 | 101 |  | 100 | 2.7 | 2.7
PFPeA | 4.3 | 4.05 | 4.23 | 4.37 | 4.52 |  | 95 | 99 | 103 | 106 |  | 101 | 4.7 | 4.6
PFPeS | 2.1 | 1.97 | 2.07 | 2.11 | 1.97 |  | 94 | 98 | 100 | 94 |  | 97 | 3.3 | 3.5
PFTDA | 2.3 | 1.97 | 1.93 | 2.00 | 2.27 |  | 86 | 84 | 87 | 99 |  | 89 | 6.9 | 7.7
PFTrDA | 2.2 | 2.48 | 2.41 | 2.85 | 2.57 |  | 113 | 110 | 130 | 117 |  | 118 | 8.8 | 7.5
PFUnA | 2.2 | 1.99 | 2.11 | 2.07 | 2.14 |  | 92 | 97 | 95 | 98 |  | 96 | 2.9 | 3.1

## Slide 36: MDL data for native PFAS 1633
Chart: MDL data 1633 for native PFAS on EZPFC
| 11Cl-PF3OUdS | 3-3 FTCA | 4-2 FTS | 5-3 FTCA | 6-2 FTS | 7-3 FTCA | 8-2 FTS | 9Cl-PF3ONS | ADONA | EtFOSE | HFPO-DA | MeFOSE | N-EtFOSA | N-EtFOSAA | NFDHA | N-MeFOSA | N-MeFOSAA | PFBA | PFBS | PFDA | PFDoA | PFDoS | PFDS | PFEESA | PFHpA | PFHpS | PFHxA | PFHxS | PFMBA | PFMPA | PFNA | PFNS | PFOA | PFOS | PFOSA | PFPeA | PFPeS | PFTDA | PFTrDA | PFUnA

 | 0.12928 | 0.35036 | 0.22444 | 0.95392 | 0.15197 | 1.0834 | 0.29003 | 0.18995 | 0.09811 | 0.558 | 0.44863 | 0.36742 | 0.085885 | 0.098544 | 0.090054 | 0.1462 | 0.11317 | 0.13399 | 0.094697 | 0.077536 | 0.087848 | 0.089806 | 0.073509 | 0.14101 | 0.053251 | 0.091577 | 0.058623 | 0.092243 | 0.080341 | 0.067524 | 0.12097 | 0.062587 | 0.10533 | 0.11587 | 0.069293 | 0.04964 | 0.080423 | 0.083326 | 0.093991 | 0.069638

## Slide 37: Method Detection Limit data for 1633
Compound Method |  |  |  | In ng/L |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Name |  | Tareget Amount ng/L |  | MDL-1 | MDL-2 | MDL-3 | MDL-4 | MDL-5 | MDL-6 | MDL-7 | MDL-8 | MDL-9 | MDL-10 | MDL-11 | MDL-12 |  | STDEV |  | MDL
11Cl-PF3OUdS |  | 1.00 |  | 0.9757 | 0.8461 | 0.8848 | 0.8676 | 0.903 | 0.9562 | 0.9295 | 1.001 | 0.9269 | 0.8606 | 0.8928 | 0.8952 |  | 0.05 |  | 0.13
3-3 FTCA |  | 1.16 |  | 1.1076 | 1.0061 | 1.0523 | 0.7624 | 1.008 | 1.0535 | 0.8077 | 1.1272 | 0.8627 | 0.8681 | 1.1234 | 1.0782 |  | 0.13 |  | 0.35
4-2 FTS |  | 1.31 |  | 1.2138 | 1.2403 | 1.2292 | 1.12 | 1.1484 | 1.3895 | 1.2266 | 1.3185 | 1.1732 | 1.1413 | 1.3365 | 1.2441 |  | 0.08 |  | 0.22
5-3 FTCA |  | 6.26 |  | 6.4841 | 5.9048 | 5.5367 | 5.5774 | 6.0513 | 5.9923 | 5.4599 | 5.3063 | 5.4973 | 6.0996 | 5.6657 | 6.1143 |  | 0.35 |  | 0.95
6-2 FTS |  | 1.21 |  | 1.2059 | 1.1808 | 1.1303 | 1.1957 | 1.203 | 1.2985 | 1.2592 | 1.1853 | 1.2621 | 1.1807 | 1.1687 | 1.3155 |  | 0.06 |  | 0.15
7-3 FTCA |  | 6.34 |  | 6.367 | 6.1878 | 5.4119 | 5.3315 | 6.0653 | 6.2616 | 6.213 | 5.8661 | 5.2776 | 6.2892 | 6.0647 | 6.234 |  | 0.40 |  | 1.08
8-2 FTS |  | 1.33 |  | 1.2039 | 1.299 | 1.2643 | 1.389 | 1.317 | 1.1943 | 1.5686 | 1.2324 | 1.2724 | 1.2325 | 1.3068 | 1.4187 |  | 0.11 |  | 0.29
9Cl-PF3ONS |  | 1.09 |  | 1.1451 | 0.9936 | 1.0535 | 0.9826 | 1.0667 | 1.0434 | 0.9971 | 1.0751 | 1.1198 | 1.0277 | 0.9342 | 1.1701 |  | 0.07 |  | 0.19
ADONA |  | 0.89 |  | 0.9331 | 0.8955 | 0.9211 | 0.8563 | 0.8665 | 0.9005 | 0.8241 | 0.8555 | 0.8582 | 0.8953 | 0.8385 | 0.9277 |  | 0.04 |  | 0.10
EtFOSE |  | 3.06 |  | 3.1171 | 2.9492 | 2.8939 | 2.8205 | 2.7337 | 2.9667 | 3.0383 | 2.9994 | 3.5478 | 2.9956 | 3.1121 | 3.1652 |  | 0.21 |  | 0.56
HFPO-DA |  | 1.16 |  | 1.1641 | 1.3673 | 1.5113 | 1.0828 | 1.0109 | 1.0609 | 1.1359 | 1.3796 | 1.1205 | 1.2871 | 0.9968 | 1.0701 |  | 0.17 |  | 0.45
MeFOSE |  | 3.00 |  | 2.5702 | 2.7387 | 2.6963 | 2.6539 | 2.8431 | 2.9566 | 2.7913 | 2.9272 | 2.8156 | 2.5827 | 2.5617 | 2.8164 |  | 0.14 |  | 0.37
N-EtFOSA |  | 0.27 |  | 0.3248 | 0.2129 | 0.2622 | 0.2651 | 0.2489 | 0.2446 | 0.2385 | 0.2225 | 0.2738 | 0.2605 | 0.2469 | 0.3043 |  | 0.03 |  | 0.09
N-EtFOSAA |  | 0.30 |  | 0.2845 | 0.2739 | 0.2375 | 0.2527 | 0.2837 | 0.2303 | 0.2095 | 0.2888 | 0.3021 | 0.2625 | 0.2115 | 0.3256 |  | 0.04 |  | 0.10
NFDHA |  | 0.64 |  | 0.6186 | 0.619 | 0.5583 | 0.6562 | 0.6746 | 0.5904 | 0.5982 | 0.6066 | 0.574 | 0.5886 | 0.5884 | 0.625 |  | 0.03 |  | 0.09
N-MeFOSA |  | 0.31 |  | 0.2471 | 0.3268 | 0.2514 | 0.2368 | 0.2816 | 0.3739 | 0.2901 | 0.3545 | 0.3193 | 0.232 | 0.3859 | 0.3278 |  | 0.05 |  | 0.15
N-MeFOSAA |  | 0.28 |  | 0.3117 | 0.2472 | 0.2321 | 0.2977 | 0.2384 | 0.2612 | 0.2864 | 0.2534 | 0.2638 | 0.3746 | 0.2339 | 0.3021 |  | 0.04 |  | 0.11
PFBA |  | 1.08 |  | 1.0962 | 1.159 | 1.1025 | 1.0075 | 1.1083 | 1.1955 | 1.173 | 1.1283 | 1.1204 | 1.1415 | 1.172 | 1.1056 |  | 0.05 |  | 0.13
PFBS |  | 0.28 |  | 0.3285 | 0.2689 | 0.2388 | 0.2611 | 0.2751 | 0.3131 | 0.221 | 0.3002 | 0.2619 | 0.319 | 0.2321 | 0.2757 |  | 0.03 |  | 0.09
PFDA |  | 0.27 |  | 0.2506 | 0.2909 | 0.2361 | 0.2176 | 0.2595 | 0.2759 | 0.2616 | 0.3261 | 0.2425 | 0.2495 | 0.2792 | 0.2476 |  | 0.03 |  | 0.08
PFDoA |  | 0.29 |  | 0.3323 | 0.2606 | 0.2292 | 0.2169 | 0.2683 | 0.2693 | 0.2342 | 0.209 | 0.2512 | 0.2323 | 0.2593 | 0.2436 |  | 0.03 |  | 0.09
PFDoS |  | 0.29 |  | 0.2192 | 0.256 | 0.2896 | 0.2259 | 0.2232 | 0.267 | 0.2175 | 0.2738 | 0.2151 | 0.2079 | 0.2143 | 0.3014 |  | 0.03 |  | 0.09
PFDS |  | 0.25 |  | 0.2301 | 0.1757 | 0.1765 | 0.2025 | 0.2176 | 0.2154 | 0.2466 | 0.2313 | 0.1801 | 0.2055 | 0.2559 | 0.2347 |  | 0.03 |  | 0.07
PFEESA |  | 0.69 |  | 0.7128 | 0.6682 | 0.6493 | 0.5944 | 0.6329 | 0.7684 | 0.6109 | 0.6574 | 0.5812 | 0.6736 | 0.622 | 0.6703 |  | 0.05 |  | 0.14
PFHpA |  | 0.26 |  | 0.2297 | 0.2846 | 0.2933 | 0.2427 | 0.2696 | 0.251 | 0.2392 | 0.2503 | 0.2656 | 0.28 | 0.2552 | 0.2479 |  | 0.02 |  | 0.05
PFHpS |  | 0.28 |  | 0.2574 | 0.2908 | 0.326 | 0.2877 | 0.2886 | 0.3607 | 0.2466 | 0.2722 | 0.2683 | 0.3081 | 0.3061 | 0.2464 |  | 0.03 |  | 0.09
PFHxA |  | 0.28 |  | 0.2897 | 0.2576 | 0.2562 | 0.2579 | 0.2552 | 0.2902 | 0.2793 | 0.3301 | 0.2716 | 0.2875 | 0.2799 | 0.2912 |  | 0.02 |  | 0.06
PFHxS |  | 0.28 |  | 0.2227 | 0.3127 | 0.2622 | 0.246 | 0.2643 | 0.2726 | 0.3009 | 0.2923 | 0.2666 | 0.1995 | 0.2697 | 0.3092 |  | 0.03 |  | 0.09
PFMBA |  | 0.54 |  | 0.539 | 0.5606 | 0.5443 | 0.5149 | 0.5315 | 0.574 | 0.5406 | 0.6259 | 0.5466 | 0.5749 | 0.5672 | 0.5869 |  | 0.03 |  | 0.08
PFMPA |  | 0.50 |  | 0.4847 | 0.4793 | 0.4858 | 0.4529 | 0.4525 | 0.5001 | 0.4696 | 0.4255 | 0.4639 | 0.4289 | 0.4308 | 0.4424 |  | 0.02 |  | 0.07
PFNA |  | 0.27 |  | 0.2852 | 0.3358 | 0.2602 | 0.2634 | 0.238 | 0.3386 | 0.3071 | 0.3041 | 0.1958 | 0.2127 | 0.2647 | 0.2618 |  | 0.04 |  | 0.12
PFNS |  | 0.26 |  | 0.2396 | 0.2515 | 0.2648 | 0.2273 | 0.2186 | 0.2847 | 0.2626 | 0.2727 | 0.2753 | 0.2247 | 0.2501 | 0.2831 |  | 0.02 |  | 0.06
PFOA |  | 0.30 |  | 0.261 | 0.2558 | 0.1974 | 0.2901 | 0.2698 | 0.2128 | 0.2429 | 0.2625 | 0.2844 | 0.3486 | 0.2896 | 0.2675 |  | 0.04 |  | 0.11
PFOS |  | 0.26 |  | 0.3029 | 0.2816 | 0.2597 | 0.2627 | 0.2448 | 0.3093 | 0.2937 | 0.2765 | 0.2633 | 0.2575 | 0.4074 | 0.2837 |  | 0.04 |  | 0.12
PFOSA |  | 0.28 |  | 0.2943 | 0.2071 | 0.2477 | 0.2558 | 0.2722 | 0.2591 | 0.274 | 0.2944 | 0.2621 | 0.2323 | 0.2797 | 0.2812 |  | 0.03 |  | 0.07
PFPeA |  | 0.53 |  | 0.5197 | 0.5177 | 0.5318 | 0.4851 | 0.5124 | 0.5336 | 0.5397 | 0.5596 | 0.5282 | 0.5379 | 0.5188 | 0.5156 |  | 0.02 |  | 0.05
PFPeS |  | 0.25 |  | 0.3187 | 0.3015 | 0.2294 | 0.2379 | 0.2541 | 0.2346 | 0.2725 | 0.2498 | 0.3018 | 0.2523 | 0.2528 | 0.2857 |  | 0.03 |  | 0.08
PFTDA |  | 0.30 |  | 0.2558 | 0.2445 | 0.2144 | 0.2632 | 0.2519 | 0.2855 | 0.3153 | 0.3078 | 0.3042 | 0.2542 | 0.2394 | 0.2742 |  | 0.03 |  | 0.08
PFTrDA |  | 0.26 |  | 0.2658 | 0.2708 | 0.2303 | 0.2448 | 0.3257 | 0.2801 | 0.2462 | 0.2674 | 0.3147 | 0.2731 | 0.3081 | 0.3411 |  | 0.03 |  | 0.09
PFUnA |  | 0.29 |  | 0.2569 | 0.2504 | 0.2495 | 0.2524 | 0.2639 | 0.2939 | 0.2639 | 0.2902 | 0.2471 | 0.1995 | 0.2852 | 0.2803 |  | 0.03 |  | 0.07

## Slide 38: Native PFAS 1633 in tap water from two locations
Compound Method |  |  | Tap Water location 1 |  | Tap Water location 1 |  | Tap Water location 1 |  | Tap Water location 1 |  | Tap Water location 1 |  | Tap water location 2 |  | Tap water location 2 |  | Tap water location 2 | 
Name |  |  | Final Conc.-01 ng/L |  | Final Conc.-02 ng/L |  | Final Conc.-03 ng/L |  | Final Conc.-04 ng/L |  | Final Conc.-05 ng/L |  | Final Conc.-01 ng/L |  | Final Conc.-02 ng/L |  | Final Conc.-03 ng/L | 
11Cl-PF3OUdS |  |  | 0.0000 |  | 0.0000 |  | 0.0000 |  | 0.0000 |  | 0.0000 |  | 0.0000 |  | 0.0000 |  | 0.0000 | 
3-3 FTCA |  |  | 0.0000 |  | 0.0000 |  | 0.0000 |  | 0.0000 |  | 0.0000 |  | 0.0234 |  | 0.0000 |  | 0.0000 | 
4-2 FTS |  |  | 0.0146 |  | 0.0446 |  | 0.0330 |  | 0.0268 |  | 0.0156 |  | 0.0908 |  | 0.1206 |  | 0.2044 | 
5-3 FTCA |  |  | 0.0000 |  | 0.0000 |  | 0.0000 |  | 0.0000 |  | 0.0000 |  | 0.0000 |  | 0.0000 |  | 0.0000 | 
6-2 FTS |  |  | 0.1434 |  | 0.1154 |  | 0.0282 |  | 0.0950 |  | 0.0798 |  | 24.7672 |  | 17.3236 |  | 86.8058 | 
7-3 FTCA |  |  | 0.0000 |  | 0.0000 |  | 0.0000 |  | 0.0000 |  | 0.0000 |  | 0.0000 |  | 0.0000 |  | 0.0000 | 
8-2 FTS |  |  | 0.0000 |  | 0.0000 |  | 0.0000 |  | 0.0000 |  | 0.0202 |  | 0.0000 |  | 0.0000 |  | 0.0000 | 
9Cl-PF3ONS |  |  | 0.0000 |  | 0.0000 |  | 0.0000 |  | 0.0000 |  | 0.0000 |  | 0.0000 |  | 0.0000 |  | 0.0000 | 
ADONA |  |  | 0.0000 |  | 0.0000 |  | 0.0000 |  | 0.0000 |  | 0.0000 |  | 0.0000 |  | 0.0000 |  | 0.0000 | 
EtFOSE |  |  | 0.0882 |  | 0.2222 |  | 0.1464 |  | 0.0848 |  | 0.1984 |  | 0.1234 |  | 0.0928 |  | 0.0736 | 
HFPO-DA |  |  | 0.0000 |  | 0.0000 |  | 0.0000 |  | 0.0000 |  | 0.0000 |  | 0.0000 |  | 0.0000 |  | 0.0000 | 
MeFOSE |  |  | 0.1272 |  | 0.1502 |  | 0.0666 |  | 0.1212 |  | 0.0862 |  | 0.0642 |  | 0.0994 |  | 0.0412 | 
N-EtFOSA |  |  | 0.0000 |  | 0.0000 |  | 0.0000 |  | 0.0134 |  | 0.0000 |  | 0.0000 |  | 0.0000 |  | 0.0000 | 
N-EtFOSAA |  |  | 0.0000 |  | 0.0000 |  | 0.0000 |  | 0.0000 |  | 0.0000 |  | 0.0236 |  | 0.0152 |  | 0.0000 | 
NFDHA |  |  | 0.0070 |  | 0.0192 |  | 0.0152 |  | 0.0182 |  | 0.0078 |  | 0.0072 |  | 0.0234 |  | 0.0196 | 
N-MeFOSA |  |  | 0.0294 |  | 0.0036 |  | 0.0094 |  | 0.0000 |  | 0.0356 |  | 0.0000 |  | 0.0090 |  | 0.0154 | 
N-MeFOSAA |  |  | 0.0000 |  | 0.0000 |  | 0.0000 |  | 0.0064 |  | 0.0116 |  | 0.0000 |  | 0.0000 |  | 0.0000 | 
PFBA |  |  | 1.5770 |  | 1.3316 |  | 1.3872 |  | 1.4132 |  | 1.4016 |  | 1.1606 |  | 1.3030 |  | 1.4006 | 
PFBS |  |  | 1.6218 |  | 1.2796 |  | 1.2782 |  | 1.4984 |  | 1.4660 |  | 1.4100 |  | 1.1902 |  | 1.4956 | 
PFDA |  |  | 0.0718 |  | 0.0974 |  | 0.0890 |  | 0.0626 |  | 0.0706 |  | 0.0000 |  | 0.0000 |  | 0.0000 | 
PFDoA |  |  | 0.0000 |  | 0.0000 |  | 0.0000 |  | 0.0000 |  | 0.0000 |  | 0.0000 |  | 0.0000 |  | 0.0000 | 
PFDoS |  |  | 0.0000 |  | 0.0000 |  | 0.0000 |  | 0.0000 |  | 0.0000 |  | 0.0000 |  | 0.0000 |  | 0.0000 | 
PFDS |  |  | 0.0000 |  | 0.0000 |  | 0.0000 |  | 0.0000 |  | 0.0000 |  | 0.0000 |  | 0.0000 |  | 0.0000 | 
PFEESA |  |  | 0.0000 |  | 0.0000 |  | 0.0000 |  | 0.0000 |  | 0.0000 |  | 0.0000 |  | 0.0000 |  | 0.0000 | 
PFHpA |  |  | 1.0702 |  | 0.9342 |  | 0.9920 |  | 0.9988 |  | 0.8530 |  | 0.8032 |  | 0.8514 |  | 0.8058 | 
PFHpS |  |  | 0.0212 |  | 0.0272 |  | 0.0342 |  | 0.0116 |  | 0.0000 |  | 0.0292 |  | 0.0414 |  | 0.0332 | 
PFHxA |  |  | 1.8204 |  | 1.7654 |  | 1.7784 |  | 1.8550 |  | 1.7464 |  | 1.0906 |  | 1.2070 |  | 1.2286 | 
PFHxS |  |  | 0.7156 |  | 0.6920 |  | 0.6024 |  | 0.9908 |  | 0.8098 |  | 1.1624 |  | 1.2360 |  | 1.0748 | 
PFMBA |  |  | 0.0054 |  | 0.0022 |  | 0.0064 |  | 0.0056 |  | 0.0000 |  | 0.0022 |  | 0.0036 |  | 0.0040 | 
PFMPA |  |  | 0.0014 |  | 0.0058 |  | 0.0046 |  | 0.0052 |  | 0.0010 |  | 0.0038 |  | 0.0044 |  | 0.0060 | 
PFNA |  |  | 0.4840 |  | 0.2624 |  | 0.2900 |  | 0.3934 |  | 0.4108 |  | 0.2682 |  | 0.2684 |  | 0.0964 | 
PFNS |  |  | 0.0000 |  | 0.0000 |  | 0.0000 |  | 0.0000 |  | 0.0000 |  | 0.0000 |  | 0.0000 |  | 0.0000 | 
PFOA |  |  | 2.1128 |  | 1.7522 |  | 1.7848 |  | 1.6276 |  | 1.8030 |  | 1.5536 |  | 1.9654 |  | 1.8556 | 
PFOS |  |  | 0.9254 |  | 0.8520 |  | 0.8944 |  | 0.8462 |  | 1.0024 |  | 0.9536 |  | 0.9838 |  | 1.2636 | 
PFOSA |  |  | 0.0348 |  | 0.0130 |  | 0.0268 |  | 0.0188 |  | 0.0030 |  | 0.0256 |  | 0.0304 |  | 0.0560 | 
PFPeA |  |  | 1.9106 |  | 1.6546 |  | 1.7258 |  | 1.7332 |  | 1.6934 |  | 1.3638 |  | 1.3744 |  | 1.4148 | 
PFPeS |  |  | 0.1314 |  | 0.1322 |  | 0.0982 |  | 0.1312 |  | 0.1380 |  | 0.3302 |  | 0.1154 |  | 0.3052 | 
PFTDA |  |  | 0.0000 |  | 0.0000 |  | 0.0000 |  | 0.0000 |  | 0.0000 |  | 0.0000 |  | 0.0000 |  | 0.0000 | 
PFTrDA |  |  | 0.0000 |  | 0.0000 |  | 0.0000 |  | 0.0000 |  | 0.0000 |  | 0.0000 |  | 0.0000 |  | 0.0000 | 
PFUnA |  |  | 0.0416 |  | 0.0584 |  | 0.0396 |  | 0.0244 |  | 0.0352 |  | 0.0000 |  | 0.0000 |  | 0.0000 | 

## Slide 39: Native PFAS 1633 in River Water
Compound Method |  |  | River Water |  | River Water |  | River Water | 
Name |  |  | Final Conc. ng/L |  | Final Conc. ng/L |  | Final Conc. ng/L | 
11Cl-PF3OUdS |  |  | 0.0000 |  | 0.0000 |  | 0.0000 | 
3-3 FTCA |  |  | 0.0000 |  | 0.0000 |  | 0.0000 | 
4-2 FTS |  |  | 0.1414 |  | 0.5982 |  | 0.1840 | 
5-3 FTCA |  |  | 0.0000 |  | 0.0000 |  | 0.0000 | 
6-2 FTS |  |  | 49.0880 |  | 143.2002 |  | 54.1156 | 
7-3 FTCA |  |  | 0.0000 |  | 0.0000 |  | 0.0000 | 
8-2 FTS |  |  | 0.0000 |  | 0.0000 |  | 0.0000 | 
9Cl-PF3ONS |  |  | 0.0000 |  | 0.0000 |  | 0.0000 | 
ADONA |  |  | 0.0000 |  | 0.0000 |  | 0.0000 | 
EtFOSE |  |  | 0.0484 |  | 0.0254 |  | 0.0000 | 
HFPO-DA |  |  | 0.0000 |  | 0.0000 |  | 0.0000 | 
MeFOSE |  |  | 0.0368 |  | 0.0388 |  | 0.0358 | 
N-EtFOSA |  |  | 0.0000 |  | 0.0000 |  | 0.0000 | 
N-EtFOSAA |  |  | 0.1178 |  | 0.0052 |  | 0.1104 | 
NFDHA |  |  | 0.0046 |  | 0.0194 |  | 0.0124 | 
N-MeFOSA |  |  | 0.0116 |  | 0.0000 |  | 0.0030 | 
N-MeFOSAA |  |  | 0.0752 |  | 0.0482 |  | 0.0472 | 
PFBA |  |  | 1.2922 |  | 1.3166 |  | 1.5178 | 
PFBS |  |  | 2.4348 |  | 2.3022 |  | 3.0300 | 
PFDA |  |  | 0.2762 |  | 0.0490 |  | 0.2702 | 
PFDoA |  |  | 0.0000 |  | 0.0000 |  | 0.0000 | 
PFDoS |  |  | 0.0000 |  | 0.0000 |  | 0.0000 | 
PFDS |  |  | 0.0000 |  | 0.0000 |  | 0.0000 | 
PFEESA |  |  | 0.0000 |  | 0.0000 |  | 0.0000 | 
PFHpA |  |  | 1.0380 |  | 1.2252 |  | 1.2282 | 
PFHpS |  |  | 0.0738 |  | 0.0352 |  | 0.0638 | 
PFHxA |  |  | 1.9908 |  | 2.1192 |  | 2.4204 | 
PFHxS |  |  | 1.6712 |  | 1.6714 |  | 2.2346 | 
PFMBA |  |  | 0.0000 |  | 0.0000 |  | 0.0000 | 
PFMPA |  |  | 0.0000 |  | 0.0000 |  | 0.0048 | 
PFNA |  |  | 0.3328 |  | 0.3946 |  | 0.4566 | 
PFNS |  |  | 0.0000 |  | 0.0000 |  | 0.0000 | 
PFOA |  |  | 2.8638 |  | 2.7774 |  | 3.2582 | 
PFOS |  |  | 6.0952 |  | 3.3096 |  | 8.5638 | 
PFOSA |  |  | 0.0226 |  | 0.0262 |  | 0.0490 | 
PFPeA |  |  | 1.8224 |  | 1.9592 |  | 2.1968 | 
PFPeS |  |  | 0.2370 |  | 0.1780 |  | 0.2588 | 
PFTDA |  |  | 0.0000 |  | 0.0000 |  | 0.0000 | 
PFTrDA |  |  | 0.0000 |  | 0.0000 |  | 0.0000 | 
PFUnA |  |  | 0.0402 |  | 0.0278 |  | 0.0496 | 

## Slide 40: Native PFAS 1633 in Well Water
Compound Method |  | Well water-1 |  | Well water-2 |  | Well water-3 | 
Name ng/L |  | Final Conc. ng/L |  | Final Conc. ng/L |  | Final Conc. ng/L | 
11Cl-PF3OUdS |  | 0.00 |  | 0.00 |  | 0.00 | 
3-3 FTCA |  | 0.04 |  | 0.00 |  | 0.00 | 
4-2 FTS |  | 0.19 |  | 0.15 |  | 0.12 | 
5-3 FTCA |  | 0.00 |  | 0.00 |  | 0.00 | 
6-2 FTS |  | 38.72 |  | 26.24 |  | 7.79 | 
7-3 FTCA |  | 0.00 |  | 0.00 |  | 0.00 | 
8-2 FTS |  | 0.00 |  | 0.00 |  | 0.00 | 
9Cl-PF3ONS |  | 0.00 |  | 0.00 |  | 0.00 | 
ADONA |  | 0.00 |  | 0.00 |  | 0.00 | 
EtFOSE |  | 0.02 |  | 0.00 |  | 0.00 | 
HFPO-DA |  | 0.05 |  | 0.03 |  | 0.02 | 
MeFOSE |  | 0.02 |  | 0.02 |  | 0.02 | 
N-EtFOSA |  | 0.00 |  | 0.00 |  | 0.01 | 
N-EtFOSAA |  | 0.00 |  | 0.00 |  | 0.01 | 
NFDHA |  | 0.00 |  | 0.01 |  | 0.00 | 
N-MeFOSA |  | 0.00 |  | 0.00 |  | 0.00 | 
N-MeFOSAA |  | 0.00 |  | 0.00 |  | 0.00 | 
PFBA |  | 1.55 |  | 1.70 |  | 1.54 | 
PFBS |  | 1.32 |  | 1.41 |  | 1.32 | 
PFDA |  | 0.04 |  | 0.06 |  | 0.05 | 
PFDoA |  | 0.00 |  | 0.00 |  | 0.00 | 
PFDoS |  | 0.00 |  | 0.00 |  | 0.00 | 
PFDS |  | 0.00 |  | 0.00 |  | 0.00 | 
PFEESA |  | 0.00 |  | 0.00 |  | 0.00 | 
PFHpA |  | 0.81 |  | 0.88 |  | 0.92 | 
PFHpS |  | 0.03 |  | 0.05 |  | 0.02 | 
PFHxA |  | 1.97 |  | 1.92 |  | 1.96 | 
PFHxS |  | 0.93 |  | 1.14 |  | 1.11 | 
PFMBA |  | 0.00 |  | 0.00 |  | 0.00 | 
PFMPA |  | 0.00 |  | 0.00 |  | 0.00 | 
PFNA |  | 0.16 |  | 0.10 |  | 0.18 | 
PFNS |  | 0.00 |  | 0.00 |  | 0.00 | 
PFOA |  | 3.93 |  | 3.41 |  | 3.93 | 
PFOS |  | 0.40 |  | 0.46 |  | 0.41 | 
PFOSA |  | 0.00 |  | 0.00 |  | 0.02 | 
PFPeA |  | 1.70 |  | 1.76 |  | 1.77 | 
PFPeS |  | 0.12 |  | 0.11 |  | 0.12 | 
PFTDA |  | 0.00 |  | 0.00 |  | 0.00 | 
PFTrDA |  | 0.00 |  | 0.00 |  | 0.00 | 
PFUnA |  | 0.00 |  | 0.00 |  | 0.00 | 

## Slide 41: Competitor Comparison

## Slide 42: Summary
Automated SPE for PFAS
EconoTrace
  Fully automated, positive pressure system, automated bottle rinse, direct delivery to SuperVap Concentrator
  Designed for cleaner samples
  Modular and Expandable
TurboTrace
  Fully automated, Vacuum pump for loading “dirty samples”, automated bottle rinse, direct delivery to SuperVap Concentrator
  Designed for Drinking water and WasteWater
  Modular and Expandable
Semi Automated SPE for PFAS
EZPFC
  Low Cost, High Throughput
  2 EZPFC 12 position systems and the SuperVap PFC Concentrator for 24 samples
  Run a batch of 24 in 2 hours

## Slide 43: Information Links
EconoTrace Webpage
TurboTrace PFC Parallel Sequential Webpage
EZPFC Webpage